## Slide 1: Safe Platooning of Unmanned Aerial Vehicles via Reachability
Mo Chen, Qie Hu, Casey Mackin, Jaime Fisac,
Shankar Sastry, Claire Tomlin
2015-03-19 NASA UTM Meeting

## Slide 2: Goals
Tractable analysis of N quadrotors by restricting them into a single-file platoon
HJ reachability
  Liveness controllers
  Safety controllers
Simulations

## Slide 3: HJ Reachability
Define target set
  Models either desired or undesired states, depending on application
  Corresponding implicit surface function:
Compute reachable set
  Set of states that can reach within time horizon
  Assumes worst case disturbance if there is disturbance
  Corresponding implicit surface function:
    Obtained by solving HJ PDE

## Slide 4: Liveness controllers from reachable sets
Merging onto a highway
  Target set: desired merging point and relative velocity
  Reachable set: set of states that can reach target set
Joining platoon on highway
  Target set: desired merging point in terms of relative coordinates
  Reachable set: set of states in relative coordinates that can reach target set
Controller
  Take straight line towards target until vehicle is inside reachable set
  Use optimal control from reachable set once vehicle is inside reachable set

## Slide 5: Safety controllers
Collision avoidance
  Target set: collision box in relative states plus (union) velocity limits
  Reachable set: set of states in relative coordinates that will hit target set assuming worst case disturbance
Controller
  Use liveness controller if safe
  Use safety controller if not safe

## Slide 6: Merging onto highway
Notes: LEFT: red quadrotor merges onto highway at red circle: straight line towards target when outside of reachable set (red dotted boundary), and then optimal controller from reachable set once inside.
Blue quadrotor joins platoon behind red; straight line to blue circle (defined in the relative state) when not inside reachable set, optimal control when inside.
Must stay outside of safety reachable set at all times (dashed boundaries)
RIGHT: The first quadrotor that completes the merging onto an empty highway creates a platoon and becomes its leader, while subsequent quadrotors form a platoon behind the leader in a pre-specified order.

## Slide 7: Responding to intruder
Notes: Within platoon, safety breached if there could be a collision within next 1.5 seconds.
W.r.t to the intruder, safety is breached if there could be a collision within next 3 seconds.

## Slide 8: Faulty quad-rotor in platoon

## Slide 9: Faulty quad-rotor in platoon w/ RS

## Slide 10: Dynamics
Single quadrotor dynamics
Relative coordinates
Notes: i is evader, j is pursuer

## Slide 11: Dynamics
Relative dynamics (for collision avoidance)
Augmented relative dynamics (for collision avoidance and velocity limit)
Notes: Velocity of quadrotor i needed for specifying velocity limit

## Slide 12: HJ Reachability
HJ PDE for :
Elimination of complexity issues
  Decoupled HJ formulation