## Slide 1: Multi-Agent Collision Avoidance
via Hamilton-Jacobi reachability and Mixed Integer Programming

## Slide 2: Problem set up
vehicles each with its own destination
Must avoid each other’s danger zones
Targets
Vehicle
Danger zone

## Slide 3: Background
Hamilton-Jacobi reachability
  Computes reachable set – the set of states from which collision could occur
  Indicates safety level between any two vehicles
  Provides safety controller that guarantees pair wise collision avoidance
  Intractable for multiple vehicles
Mixed integer programming
  Takes safety values and joint configuration into account
  Provides avoidance logic in multi-vehicle systems
  Produces joint collision avoidance maneuver for multiple vehicles

## Slide 4: HJ Reachability for Collision Avoidance
For a dynamical system with given
  Dynamics
  Target states
Determines, with guarantees
  Set of states from which the system can be driven to the target state
Guarantees pair wise collision avoidance
Reachable set
Target set

## Slide 5: Mixed Integer Program for Collision Avoidance
Optimization intuition:
Cooperatively resolve as many pair wise conflicts as possible
Subject to
  Efficient use of control authority
    At most one vehicle in each pair wise conflict performs avoidance maneuver
    Avoid multiple vehicles at once where possible
  Limited avoidance capabilities of each vehicle
    Allows non-conflicted vehicles to “help” with joint avoidance
Dictates cooperative avoidance logic between all vehicle pairs

## Slide 6: Three-vehicle safety guarantee
Joint avoidance maneuvers guarantee collision avoidance for three vehicles
Previously not possible using only HJ reachability
[3-vehicle VIDEO HERE]

## Slide 7: Multi-vehicle performance
[NAÏVE APPROACH VIDEO]
[NEW APPROACH VIDEO]

## Slide 8: Details of basic optimzation
: avoidance priority
: whether vehicle avoids
Maximize number of resolved conflicts
Efficient use of control authority
Avoidance limitations