## Slide 1
TFM
HWY Reachable sets
Safety Reachable sets
Platoon Reachable sets
Highways
Highway
Platoon
Platoon
vehicle
Platoon
vehicle
State
vehicle
Type
State
vehicle
Type

## Slide 2
TFM
Base create platoon reachable set
Highway orientation, velocity
Target entry point
Vehicle type
Waypoints
(control sequence)
Base join platoon reachable set
Highway orientation, velocity
Platoon next available position
Vehicle types
Waypoints
(control sequence)
Base safety reachable set
Vehicle types
Vehicle states
Waypoints
(control sequence)

## Slide 3: Vehicle responsibilities
Each vehicle registers itself with TFM before it flies
  Deregisters when vehicle gets to destination
Each vehicle reigsters platoon with TFM when it forms a platoon
  Deregisters when platoon is dissolved
TFM
vehicle
vehicle
vehicle
Platoon
vehicle

## Slide 4: TFM Responsibilities
Maintain a list of ”active agents”
  Includes free vehicles, platoons
  Excludes follower vehicles
For each active agent, check safety against all other active agents
  Combinatorial explosion here, but most of the time, only distances need to be checked
For each vehicle in the platoon, check safety with neighbors

## Slide 5
TFM
vehicle
vehicle
vehicle
Platoon
vehicle
vehicle
vehicle
Platoon
vehicle
vehicle
vehicle

## Slide 6: Number of safety checks
All N vehicles are free:
  N choose 2
  Combinatorial, doesn’t necessarily guarantee safety especially for large N
  N = 15 => 105 checks
n free vehicles + p platoons with k vehicles in each
  (n+p) choose 2 + (k-1)*p
  p = 3, k = 4, n = 3 (so that n + pk = N = 15) => 6 choose 2 + 3 * 3 = 24 checks

## Slide 7: Type of safety checks
Active agents
  Quick check: distance
  Detailed check: safety reachable set
Vehicles within platoons
  Quick check: state error (with respect to phantom state)
  Detailed check: safety reachable set