## Slide 1
Safe Platooning of Unmanned Aerial Vehicles via Reachability
Mo Chen, Qie Hu, Casey Mackin, Jaime F. Fisac, Anayo K. Akametalu, Claire Tomlin
Hybrid modes for vehicles in platoons.
Two Highways
2 of the vehicles (orange, light blue) in the 4-vehicle platoon changes highway and join the 3-vehicle platoon. The remaining 2 vehicles (purple, dark blue) remain on the same highway.
Safety
Both vehicles must use safe controller on the boundary of safety reachable set
Liveness
Red vehicle: merges onto the highway to form a platoon
Blue vehicle: joins platoon
Move in a straight line towards target until inside liveness reachable set
Follow optimal control given by livenes reachable set
Intruder Vehicle
Leader vehicle (blue) unaffected by intruder. Remaining 3 vehicles (orange, yellow, purple) deviate to avoid collision with intruder, and return to highway when safe again.
For a dynamical system with given
Dynamics
Target set of states
Reachable set
Set of states from which the system can be driven into the target set under worst-case disturbance
Guarantees both liveness and safety
Constructs optimal control
Simulations
Air highways minimize total cost: Cost of accidents, fuel, noise pollution, etc.
In ascending cost: Water, low population land, high population land, airports.
Resulting highway placement shows “trunks” and “branches”.
Shortest paths from Concord to 9 other cities in the San Francisco Bay Area.
Reaction of a 4-vehicle platoon on a highway to an intruder.
Cross-over of a 4-vehicle platoon on one highway with a 3-vehicle platoon on a second highway.
Reachability
Safety and Liveness
Air Highways
Platoons
Electrical Engineering and Computer Sciences, UC Berkeley